## Slide 1: The role of remote Photoplethysmography in Musical Biofeedback Systems for Stress Reduction and Consciousness Regulation
Univers Condensed
Fabian Winkelmann
Student ID: 1284247

## Slide 2: Structure
Univers Condensed
Introduction
Stress
Remote Photoplethysmography
Musical Biofeedback
Regeneration and Consciousness Regulation
Case Studies
Conclusion

## Slide 3
Introduction
Stress changes the heart rate1
Plethysmography: Measurement of pulse waves2
Photoplethysmography (PPG): ... using light reflectance2
remote PPG (rPPG): … via digital camera (contactless)2
Biofeedback: Real-time loop returning physiological data3
Musical Biofeedback: Auditory feedback loop using music3
Musical Biofeedback Loop: Real-time translation of physiological rPPG data into intuitive musical biofeedback
Source: Own illustration
[1] cf. Mcewen2017neurobiology, [2] cf. verkruysse2008remote, [3] cf. giggins2013biofeedback

## Slide 4
Stress
Protective Response: Short-term mobilization is a vital survival mechanism1
Maladaptive Coping: Harmless situations trigger stress, leading to harmful habits (smoking, drinking)1
Heart Rate (HR): Beats per minute – represents the quantity of heart activity2
Heart Rate Variability (HRV): Time variation between consecutive beats – represents the quality of heart activity2
The figure illustrates the separate components that the brain takes into account when releasing stress1
[1] cf. Mcewen2017neurobiology [2] cf. shaffer2017overview

## Slide 5
Remote Photoplethysmography (foundation)
Absorption: Blood volume changes modulate light absorption with each beat2
Green Channel: Provides the strongest signal2
Target Areas: Cheeks offer the highest signal-to-noise ratio: easily accessible, exposed3
Spectral sensitivity of the PPG signal. Green light exhibits the highest amplitude, making it the most reliable channel for non-contact heart rate monitoring.1
[1] cf. dehaan2013chrom, [2] verkruysse2008remote,
[3] cf. lempe2013roi
The quality of the rPPG signal in the face. Blue shows low activity and red high activity3

## Slide 6
Remote Photoplethysmography (Signal extraction overview)
[1] cf. poh2010non, [2] cf. dehaan2013chrom [3] cf. Debnath25
Blind Source Separation
  Separation of pulse and noise based on statistical independence1
Physics based Models (CHROM)
  Principle: uses skin-light-reflection properties for robust real-time tracking2
Deep Learning Models
  Principle: Uses neural networks high accuracy3

## Slide 7
Remote Photoplethysmography (Blind Source Separation)
Signal Mixture: The camera image as a mixture of independent sources (Pulse, Light, Motion)1
Mathematical Tool: Uses algorithms like JADE to separate the signals1
Signal Refinement (Filtering)1
  Bandpass Limit: Restrict data to 45-240BPM
  Fast Fourier Transform Analysis: find the strongest periodic frequency (the Heart rate)
  Outlier Rejection: Prevents unrealistic jumps
Limitation1:
  Component Misidentification: In extreme light or motion, the wrong signal (light instead of pulse) is picked
  Requires a long data window (30 seconds)
Separating independent sources from raw skin color channels (RGB) using the JADE algorithm for rPPG1
[1] cf. poh2010non

## Slide 8
Remote Photoplethysmography (CHROM)
Physicsbased alternative: Chrominance-based method1
Camera sees:1
  Intensity: Brightness of light
  Specular Reflection: Mirror-like glare on the surface
  Static Skin Color: The constant tissue color
2D-Projection RGB signals are projected onto a plane perpendicular to the standard skin tone 1
Noise cancellation: A clean, movement-robust pulse signal1
Bandpass Filtering (0.7-4.0Hz) -> matching the human heart rate (42-240BPM)1
Fast Fourier Transform: Identifies the strongest periodic signal to determine the heart rate1
[1] cf. dehaan2013chrom
The illustration depicts light reflection on the skin 1

## Slide 9
Remote Photoplethysmography (CHROM)
Accuracy 98 % in stable conditions, 92 % correlation with medical sensors (ground truth)1
The "Motion" Advantage: Maintains a 48% success rate under heavy movement – where BSS models drop to a failing 4-11%1
Low latency: Only 1.6s (vs 30s with BSS)1
Diversity: Robust performance across all skin tones1
[1] cf. dehaan2013chrom

## Slide 10
Remote Photoplethysmography (Deep Learning Models)
Transition to End-to-End Deep Learning Models1
Fully automated: No manual Face/ROI selection required1
Data challenges:1
  Significant lack of large-scale, high-quality datasets
  Underrepresentation of diverse age groups and skin pigmentations
Mobile Optimization: Ongoing research into lightweight models for real-time deployment on smartphone hardware1
[1] cf. Debnath25

## Slide 11
Musical Biofeedback
Ecological Perception:1
  Uses natural associations (e.g. distance) to represent intensity
  Example: Decreasing volume mimics a sound source moving away, making data changes intuitive
Data-to-Music Transformation:1
  direct transformation of heartbeat data into an auditory stream
  Continuous parameter mapping: ensures immediate, fluid feedback of physiological changes
[1] cf. dubus2013systematic

## Slide 12
Regeneration and Consciousness Regulation
Cardiovascular Synchronization1
  Resonance Frequency: Achieved at ~6 breaths per minute
  Harmonic State: Heart rate and blood pressure synchronize for maximum efficiency
  Optimized gas exchange in the lungs
  Less strain on the cardiovascular system
Physiological Impact1
  Deep Relaxation Response in the body
  The auditory signal acts as a meditative anchor
Mindfulness2
  Enhances sensitivity to thoughts and emotional states
  Promotes an attitude of curiosity, openness and acceptance
  Helps to perceive the internal state without judgement
[1] cf. lehrer2014heart, [2] cf. bishop2004mindfulness

## Slide 13
Case Studies (Unwind System)
Concept: Nature soundscapes with sedative music to guide relaxation1
HRV Sonification1:
  Wind Mapping: Heart Rate Variability (HRV) is mapped to wind sounds
  Users adapt their breathing to transform the wind into a smooth, consistent sine wave
Adaptive Soundscape1:
  LOW HRV (Stress): Environment becomes busy and complex
  High HRV (Relaxed): Soundscape becomes simple, transparent and calm
[1] cf. yu2018unwind
The illustration depicts the feedback loop of the Unwind System1

## Slide 14
Case Studies (Unwind System)
Key Results:1
  Significant reduction in both heart rate and respiration rate in comparison to the control group
  70% of participants used the nature sounds to visualize scenes, significantly improving focus and immersion.
[1] cf. yu2018unwind
The illustration depicts the feedback loop of the Unwind System1

## Slide 15
Case Studies (MuseTM Headband )
The concept: Lowering the entry barrier for meditation through real-time brainwave measurement1
Daily attention training with feedback through smartphone app1
Key Findings:1
  Stress Reduction: The experimental group recorded a 7% decrease after 2 weeks and 14% after 4 weeks
  Mental Performance: Improved concentration levels and superior impulse control during complex tasks
  Control Group: Showed no significant changes in stress or performance levels
Real-time feedback is the decisive factor1
[1] cf. app7121280
Subject wearing the Muse™ EEG headband during a neurofeedback session.1

## Slide 16
Conclusion
The Core Metric: Heart Rate Variability (HRV)1
  HRV provides significantly deeper physiological insights than simple Heart Rate (BPM)
Technical Strategy: 2
  Choosing CHROM for its computational efficiency and real-time capabilities
The Competitive Edge:
  Unlike Blind Source Separation3, CHROM requires shorter observation windows and effectively identifies the correct color channels 2
  Superior to Deep Learning: CHROM is robust against noise without the massive resource intensity or dataset bias of AI models4
Musical Biofeedback Loop: Real-time translation of physiological rPPG data into intuitive musical biofeedback
Source: Own illustration
[1] cf. shaffer2017overview, [2] dehaan2013chrom, [3] cf. poh2010non, [4] cf. Debnath25

## Slide 17
Conclusion
The mapping Process1:
  Continuous Mapping: instant, fluid audio stream
  Sound Design: Calm State = Calm Sound – non intrusive soundscapes to reinforce relaxation
Evidence-Based Systems:
  Unwind System: uses nature sounds for feedback2
  Muse™: uses real-time loops to increase stress awareness and control3
Musical Biofeedback Loop: Real-time translation of physiological rPPG data into intuitive musical biofeedback
Source: Own illustration
[1] cf. dubus2013systematic [2] cf. yu2018unwind [3] cf. app7121280

## Slide 18
https://medium.com/@zurister/depth-wise-convolution-and-depth-wise-separable-convolution-37346565d4ec
Future Outlook
Potential: Monitor stress at work (office)
Trend: Small AI models for laptops or mobiles
Efficiency: Cost-effective (simple camera)
Privacy: High risk! Local processing only (No Cloud)

## Slide 19
https://medium.com/@zurister/depth-wise-convolution-and-depth-wise-separable-convolution-37346565d4ec
References
Identifier | Referenz
Mcewen2017neurobiology | B. S. McEwen, “Neurobiological and systemic effects of chronic stress,” Chronic Stress, vol. 1, p. 2470547017692328, 2017.
giggins2013biofeedback | O. M. Giggins, U. M. Persson, and B. Caulfield, “Biofeedback in rehabilitation,” Journal of Neuro Engineering and Rehabilitation, vol. 10, no. 1, p. 60, 2013
verkruysse2008remote | W. Verkruysse, L. O. Svaasand, and J. S. Nelson, “Remote plethysmographic imaging using ambient light,” Optics Express, vol. 16,no. 26, pp. 21 466–21 475, 2008
shaffer2017overview | F. Shaffer and J. Ginsberg, “An overview of heart rate variability metrics and norms,” Frontiers in Public Health, vol. 5, p. 258, 2017.

## Slide 20
https://medium.com/@zurister/depth-wise-convolution-and-depth-wise-separable-convolution-37346565d4ec
Identifier | Referenz
dehaan2013chrom | U. Debnath and S. Kim, “A comprehensive review of heartrate measurement using remote photoplethysmography and deep learning,” BioMedical Engineering OnLine, vol. 24, no. 1, p. 73, 2025.
lehrer2014heart | P. M. Lehrer and R. Gevirtz, “Heart rate variability biofeedback:how and why does it work?” Frontiers in Psychology, vol. 5, p. 756,2014.
bishop2004mindfulness | S. R. Bishop, M. Lau, S. Shapiro, L. Carlson, N. D. Anderson,J. Carmody, Z. V. Segal, S. Abbey, M. Speca, D. Velting et al., “Mindfulness: A proposed operational definition,” Clinical Psychology:Science and Practice, vol. 11, no. 3, pp. 230–241, 2004.

## Slide 21
https://medium.com/@zurister/depth-wise-convolution-and-depth-wise-separable-convolution-37346565d4ec
Identifier | Referenz
app7121280 | M. Balconi, D. Crivelli, G. Fronda, and I. Venturella, “Conscious, pre-conscious and unconscious mechanisms in emotional behaviour. some applications to the mindfulness approach withwearable devices,” Applied Sciences, vol. 7, no. 12, 2017. [Online].Available: https://www.mdpi.com/2076-3417/7/12/1280
yu2018unwind | B. Yu, M. Funk, J. Hu, and L. Feijs, “Unwind: a musical biofeedback for relaxation assistance,” Behaviour & Information Technology, vol. 37, no. 8, pp. 800–814, 2018. [Online]. Available: https://doi.org/10.1080/0144929X.2018.1484515
dubus2013systematic | G. Dubus and R. Bresin, “A systematic review of mapping strategies for the sonification of physical quantities,” PLoS ONE, vol. 8,no. 12, p. e82491, 2013
poh2010non | M.-Z. Poh, D. J. McDuff, and R. W. Picard, “Non-contact, automated cardiac pulse measurements using video imaging andblind source separation,” Optics Express, vol. 18, no. 10, pp. 10 762–10 774, 2010.

## Slide 22
https://medium.com/@zurister/depth-wise-convolution-and-depth-wise-separable-convolution-37346565d4ec
Identifier | Referenz
lempe2013roi | G. Lempe, S. Zaunseder, T. Wirth, S. Eck, and H. Malberg, “Roi selection for remote photoplethysmography,” in 2013 International Conference on Information Technology and Applications in Biomedicine(ITAB). IEEE, 2013, pp. 1–4.
Debnath25 | U. Debnath and S. Kim, “A comprehensive review of heartrate measurement using remote photoplethysmography and deep learning,” BioMedical Engineering OnLine, vol. 24, no. 1, p. 73, 2025